CHAPTER 3: STRINGS, VECTORS, AND ARRAYS
Among the most important library types are string, which supports variable-length character strings, and vector, which defines variable-size collections. Associated with string and vector are companion types known as iterators, which are used to access the characters in a string or the
elements in a vector.

3.1 Namespace using Declarations
scope operator = :: which says that the compiler should look in the scope of the left-hand operand for the name of the right-hand operand.
    → std::cin says that we want to use the name cin from the namespace std.

Referring to library names with this notation can be cumbersome. Fortunately, there are easier ways to use namespace members. The safest way is a using declaration

A using declaration lets us use a name from a namespace without qualifying the name with a ‘namespace_name:: prefix’.
A using declaration has the form : “using namespace::name;”
using std::cin;

A Separate using Declaration Is Required for Each Name
using std::cin;
using std::cout; using std::endl;

Headers Should Not Include using Declarations
The reason is that the contents of a header are copied into the including program’s text. If a header has a using declaration, then every program that includes that header gets that same using declaration. As a result, a program that didn’t intend to use the specified library name might encounter unexpected name conflicts.

3.2 Library string Type
A string is a variable-length sequence of characters. To use the string type, we must include the string header. Because it is part of the library, string is defined in the std namespace.
#include <string>
using std::string;
Note : In addition to specifying the operations that the library types provide, the standard also imposes efficiency requirements on implementors. As a result, library types are efficient enough for general use.

3.2.1 Defining and Initializing strings
string s1;	// default initialization; s1 is the empty string
string s2 = s1;	// s2 is a copy of s1
string s3 = "hiya";	// s3 is a copy of the string literal
string s4(10, ’c’);	// s4 is cccccccccc

Direct and Copy Forms of Initialization

using ‘=’ Copy initialization
using ‘() or {}’ Direct initialization

string s1	Default initialization s1 is the empty string.
string s2(s1)	s2 is a copy of s1.
string s2 = s1	Equivalent to s2(s1), s2 is a copy of s1.
string s3("value")	s3 is a copy of the string literal, not including the null.
string s3 = "value"	Equivalent to s3("value"), s3 is a copy of the string	literal.
string s4(n, ’c’)	Initialize s4 with n copies of the character ’c’.

3.2.2 Operations on strings
os << s	Writes s onto output stream os. Returns os.
is >> s	Reads whitespace-separated string from is into s. Returns is.
getline(is, s)	Reads a line of input from is into s. Returns is.
s.empty()	Returns true if s is empty; otherwise returns false.
s.size()	Returns the number of characters in s.
s[n]	Returns a reference to the char at position n in s; positions start at 0.
s1 + s2	Returns a string that is the concatenation of s1 and s2.
s1 = s2	Replaces characters in s1 with a copy of s2.
s1 == s2	The strings s1 and s2 are equal if they contain the same characters.
s1 != s2	Equality is case-sensitive.
<, <=, >, >=	Comparisons are case-sensitive and use dictionary ordering.

Using getline to Read an Entire Line
Sometimes we do not want to ignore the whitespace in our input. In such cases, we can use the getline function instead of the >> operator.
This function reads the given stream up to and including the first newline and stores what it read—not including the newline—in its string argument.
Like the input operator, getline returns its istream argument. As a result, we can use getline as a condition just as we can use the input operator as a condition

The string empty and size Operations

The string::size_type Type
The string class—and most other library types—defines several companion types. These companion types make it possible to use the library types in a machine-independent manner. The type size_type is one of these companion types. To use the size_type defined by string, we use the scope operator to say that the name size_type is defined in the string class.

Comparing strings
The string class defines several operators that compare strings. These operators work by comparing the characters of the strings. The comparisons are case-sensitive—upper- and lowercase versions of a letter are different characters. The equality operators (== and !=) test whether two strings are equal or unequal, respectively. Two strings are equal if they are the same length and contain the same characters. The relational operators <, <=, >, >= test whether one string is less than, less than or equal to, greater than, or greater than or equal to another. These operators use the same strategy as a (case-sensitive) dictionary:
1. If two strings have different lengths and if every character in the shorter string is equal to the corresponding character of the longer string, then the shorter string is less than the longer one.

2. If any characters at corresponding positions in the two strings differ, then the result of the string comparison is the result of comparing the first character at which the strings differ.

As an example, consider the following strings:
string str = "Hello";
string phrase = "Hello World";
string slang = "Hiya";
Using rule 1, we see that str is less than phrase. By applying rule 2, we see that
slang is greater than both str and phrase.

Assignment for strings
string st1(10, ’c’), st2;	// st1 is cccccccccc; st2 is an empty string
st1 = st2;	// assignment: replace contents of st1 with a copy of st2
// both st1 and st2 are now the empty string

Adding Two strings

string s1 = "hello, ", s2 = "world\n";
string s3 = s1 + s2;	// s3 is hello, world\n
s1 += s2;	// equivalent to s1 = s1 + s2

Adding Literals and strings
string s1 = "hello", s2 = "world";
string s3 = s1 + ", " + s2 + ’\n’;

When we mix strings and string or character literals, at least one operand to each + operator must be of string type
string s4 = s1 + ", ";	// ok: adding a string and a literal
string s5 = "hello" + ", ";	// error: no string operand
string s6 = s1 + ", " + "world";	// ok: each + has a string operand
string s7 = "hello" + ", " + s2;	// error: can’t add string literals

Note : For historical reasons, and for compatibility with C, string literals are not standard library strings. It is important to remember that these types differ when you use string literals and library strings.

Processing Every Character? Use Range-Based for
Note: These functions are defined in the cctype header.

ADVICE : USE THE C++ VERSIONS OF CLIBRARY HEADERS:
In addition to facilities defined specifically for C++, the C++ library incorporates the C library. Headers in C have names of the form name.h. The C++ versions of these headers are named cname— they remove the .h suffix and precede the name with the letter c. The c indicates that the header is part of the C library. Hence, cctype has the same contents as ctype.h, but in a form that is appropriate for C++ programs. In particular, the names defined in the cname headers are defined inside the std namespace, whereas those defined in the .h versions are not. Ordinarily, C++ programs should use the cname versions of headers and not the name.h versions. That way names from the standard library are consistently found in the std namespace. Using the .h headers puts the burden on the programmer to remember which library names are inherited from C and which are unique to C++.

Processing Every Character? Use Range-Based for
If we want to do something to every character in a string, by far the best approach is to use a statement introduced by the new standard: the range for statement. This statement iterates through the elements in a given sequence and performs some operation on each value in that sequence.
The syntactic form is:
for (declaration : expression)
statement

Table 3.3: cctype Functions
isalnum(c)	// true if c is a letter or a digit.
isalpha(c)	// true if c is a letter.
iscntrl(c)	// true if c is a control character.
isdigit(c)	// true if c is a digit.
isgraph(c)	// true if c is not a space but is printable.
islower(c)	// true if c is a lowercase letter.
isprint(c)	// true if c is a printable character (i.e., a space or a character that has a visible	// representation).
ispunct(c)	// true if c is a punctuation character (i.e., a character that is not a control
// character, a digit, a letter, or a printable whitespace).
isspace(c)	// true if c is whitespace (i.e., a space, tab, vertical tab, return, newline, or formfeed).
isupper(c)	// true if c is an uppercase letter.
isxdigit(c)	// true if c is a hexadecimal digit.
tolower(c)	// If c is an uppercase letter, returns its lowercase equivalent; otherwise returns c	// unchanged.
toupper(c)	// If c is a lowercase letter, returns its uppercase equivalent; otherwise returns
// c unchanged.

Using a Range for to Change the Characters in a string
If we want to change the value of the characters in a string, we must define the loop variable as a reference type. Remember that a reference is just another name for a given object.

string s("Hello World!!!");	// convert s to uppercase
for (auto &c : s)	// for every char in s (note: c is a reference)
c = toupper(c);	// c is a reference, so the assignment changes the char in s
cout << s << endl;

Processing Only Some Characters?
There are two ways to access individual characters in a string: We can use a subscript or an iterator.
The subscript operator (the [] operator) takes a string::size_type value that denotes the position of the character we want to access. The operator returns a reference to the character at the given position. S[0]
The value in the subscript is referred to as “a subscript” or “an index.” The index we supply can be any expression that yields an integral value. However, if our index has a signed type, its value will be converted to the unsigned type that string::size_type represents.

Before accessing the character, we check that s is not empty. Any time we use a subscript, we must ensure that there is a value at the given location. If s is empty, then s[0] is undefined.

Using a Subscript for Iteration
// process characters in s until we run out of characters or we hit a whitespace
for (decltype(s.size()) index = 0; index != s.size() && !isspace(s[index]); ++index)
s[index] = toupper(s[index]); // capitalize the current character

Warning !!!

CAUTION : SUBSCRIPTS ARE UNCHECKED
When we use a subscript, we must ensure that the subscript is in range. That is, the subscript must be >= 0 and < the size() of the string. One way to simplify code that uses subscripts is always to use a variable of type string::size_type as the subscript. Because that type is unsigned, we ensure that the subscript cannot be less than zero. When we use a size_type value as the subscript, we need to check only that our subscript is less than value returned by size(). The library is not required to check the value of an subscript. The result of using an out-of-range subscript is undefined.

3.3 Library vector Type
A vector is a collection of objects, all of which have the same type. Every object in the collection has an associated index, which gives access to that object. A vector is often referred to as a container because it “contains” other objects.
A vector is a class template.
Templates are not themselves functions or classes. Instead, they can be thought of as instructions to the compiler for generating classes or functions. The process that the compiler uses to create classes or functions from templates is called instantiation. When we use a template, we specify what kind of class or function we want the compiler to instantiate.
For a class template, we specify which class to instantiate by supplying additional information, the nature of which depends on the template. How we specify the information is always the same: We supply it inside a pair of angle brackets following the template’s name
→ vector<int> ivec; // ivec holds objects of type int

Note : vector is a template, not a type. Types generated from vector must include the element type, for example, vector<int>.

We can define vectors to hold objects of most any type. Because references are not objects we cannot have a vector of references. However, we can have vectors of most other (nonreference) built-in types and most class types. In particular, we can have vectors whose elements are themselves vectors.

It is worth noting that earlier versions of C++ used a slightly different syntax to define a vector whose elements are themselves vectors (or another template type). In the past, we had to supply a space between the closing angle bracket of the outer vector and its element type
—vector<vector<int> > rather than vector<vector<int>>.
Some compilers may require the old-style declarations for a
vector of vectors, for example, vector<vector<int> >.

3.3.1 Defining and Initializing vectors
vector<int> ivec;	// initially empty
// give ivec some values
vector<int> ivec2(ivec);	// copy elements of ivec into ivec2
vector<int> ivec3 = ivec;	// copy elements of ivec into ivec3
vector<string> svec(ivec2);	// error: svec holds strings, not ints

List Initializing a vector
Another way to provide element values, is that under the new standard, we can list initialize (§ 2.2.1, p. 43) a vector from a list of zero or more initial element values enclosed in curly braces.
vector<string> articles = {"a", "an", "the"};
we can supply a list of element values only by using list initialization in which the initializers are enclosed in curly braces. We cannot supply a list of initializers using parentheses:
→ vector<string> v1{"a", "an", "the"};	// list initialization
→ vector<string> v2("a", "an", "the");	// error

Creating a Specified Number of Elements
Creating a Specified Number of Elements We can also initialize a vector from a count and an element value. The count determines how many elements the vector will have; the value provides the initial value for each of those elements.
→ vector<int> ivec(10, -1); // ten int elements, each initialized to -1
→ vector<string> svec(10, "hi!"); // ten strings; each element is "hi!"

Value Initialization
We can usually omit the value and supply only a size. In this case the library creates a value-initialized element initializer for us. This library-generated value is used to initialize each element in the container. The value of the element initializer depends on the type of the elements stored in the vector.
If the vector holds elements of a built-in type, such as int, then the element initializer has a value of 0. If the elements are of a class type, such as string, then the element initializer is itself default initialized:
vector<int> ivec(10);	// ten elements, each initialized to 0
vector<string> svec(10);	// ten elements, each an empty string
There are two restrictions on this form of initialization:
- The first restriction is that some classes require that we always supply an explicit initializer. If
our vector holds objects of a type that we cannot default initialize, then we must supply an initial element value; it is not possible to create vectors of such types by supplying only a size.
- The second restriction is that when we supply an element count without also
supplying an initial value, we must use the direct form of initialization:

vector<T> v1	// vector that holds objects of type T. Default initialization;v1 is empty.
vector<T> v2(v1)	// v2 has a copy of each element in v1.
vector<T> v2 = v1	// Equivalent to v2(v1), v2 is a copy of the elements in v1.
vector<T> v3(n, val)	// v3 has n elements with value val.
vector<T> v4(n)	// v4 has n copies of a value-initialized object.
vector<T> v5{a,b,c . . . }	// v5 has as many elements as there are initializers; elements are	// initialized by corresponding initializers.
vector<T> v5 = {a,b,c . . . }	// Equivalent to v5{a,b,c . . . }.

List Initializer or Element Count?

vector<int> v1(10);	// v1 has ten elements with value 0
vector<int> v2{10};	// v2 has one element with value 10
vector<int> v3(10, 1);	// v3 has ten elements with value 1
vector<int> v4{10, 1};	// v4 has two elements with values 10 and 1
For vector<int>:
When we use parentheses, we are saying that the values we supply are to be used to construct the object.
When we use curly braces, {...}, we’re saying that, if possible, we want to
list initialize the object.
On the other hand,
if we use braces and there is no way to use the initializers to list initialize the object, then those values will be used to construct the object. For example, to list initialize a vector of strings, we must supply values that can be used as strings. In this case, there is no confusion about whether to list initialize the elements or construct a vector of the given size:
vector<string> v5{"hi"};	// list initialization: v5 has one element
vector<string> v6("hi");	// error: can’t construct a vector from a string literal
vector<string> v7{10};	// v7 has ten default-initialized elements
vector<string> v8{10, "hi"};	// v8 has ten elements with value "hi"

3.3.2 Adding Elements to a vector
vector<int> v2;	// empty vector
for (int i = 0; i != 100; ++i)
v2.push_back(i);	// append sequential integers to v2
// at end of loop v2 has 100 elements, values 0 . . . 99

KEY CONCEPT: VECTORS GROW EFFICIENTLY

Programming Implications of Adding Elements to a vector
Warning: The body of a range for must not change the size of the sequence over which it is iterating.

3.3.3 Other vector Operations